Foul Water Lab

Purpose:

The purpose of the lab is to purify a sample of “foul” water producing as much “clean” water as possible. Furthermore, students will figure out which filter produces the cleanest water.

Procedure:

- Obtain approximately 100ml of foul water, provided by your instructor.  Measure its volume precisely with a graduated cylinder; record your value (with units) in your data table.

- Examine, the properties of your sample: color, odor, and clarity, % transmittance (Colorimeter (PS-2121), presence of solid and or oil regions.  Record your observation in the “Before treatment” section of your data table.

| Data Table |
| --- |
|  | Color | Clarity (% transmittance) | Odor | Presence of oil | Presence of solids | Volume (ml) |
| Before treatment |  |  |  |  |  |  |
| After oil-water separation |  |  |  |  |  |  |
| After sand filtration |  |  |  |  |  |  |
| After charcoal adsorption and filtration |  |  |  |  |  |  |

Oil Water Separation

Oil and water do not noticeably dissolve in each other.  If oil and water are mixed and left undisturbed, two layers form- the oil floats on top of the water

- Place a funnel in a clay triangle supported by a ting clamp and ring stand.  Attach a rubber hose to the funnel tip as shown in the figure below

Figure 1

- Close the tuber tube by nipping it with your finger (or by using a pinch clamp).  Shake or stir the foul-water sample. Then pour about half the sample into the funnel and let it stand for a few second until the liquid layers separate.  Gently tapping my encourage oil droplets to float to the surface.

- Carefully open the tube to release the lower layer into a 150 ml beaker.  When the lower layer has drained out, quickly close the rubber tube.

- Drain the remaining layer into a second 150ml beaker.

- Repeat steps 2-4 using he remainder of your sample, adding each liquid to the correct beaker.

- Dispose of the top, oil layer as instructed by your teacher.  Observe the properties of the remaining layer and measure its volume by pouring in the filtrate it into a graduated cylinder.  Record your observation and data make sure you use the Colorimeter instrument to get the % transmittance.  Save the water sample for the next procedure.

- Wash funnel with soap and water]

Sand Filtration

A sand filter traps solid impurities that are too large to fit between the sand grains.

- Fold filter paper as shown below (Figure 2)

- Place the folded filter paper in a funnel.  Wet the paper slightly so it adheres to the funnel cone.

- Place the funnel in a clay triangle supported by the ring stand (see Figure 1).  Lower the clamp so the funnel stem extends 2-3 cm inside a 150 ml beaker.

- Add pre-moistened gravel and sand layers to the funnel that has the adhered filter paper.

- Gently pour the sample to be filtered into the cup.  Catch the filtrate (filtered water) in the 150 ml beaker.

- Dispose of the used sand and gravel according to your teacher’s instructions.  Do not pour sand or gravel into the sink!

- Observe the properties and measure the volume of the water recovered and use the colorimeter reader to get the % transmittance.

Charcoal Adsorption/Filtration

Charcoal adsorbs (attracts and holds on its surface) many substances that could give water a bad taste, odor, or cloudy appearance.  Fish tanks include charcoal filters for the same purpose

- Fold filter paper as shown below (Figure 2)

- Place the folded filter paper in a funnel.  Wet the paper slightly so it adheres to the funnel cone.

- Place the funnel in a clay triangle supported by the ring stand (see Figure 1).  Lower the clamp so the funnel stem extends 2-3 cm inside a 150 ml beaker.

- Place one teaspoon of charcoal in a 125 or 250 ml Erlenmeyer flask.

- Pour the water sample into the flask. Shake vigorously. Then gently pour the liquid thorough the filter paper.  Keep the liquid level below the top of the filter paper-no liquid should flow between the filter paper and funnel.

- If the filtrate is darkened by small charcoal particles, refilter the liquid.  Use a clean piece of moistened filter paper.

- When you are satisfied with the appearance and odor of your purified water sample, pour it into a graduated cylinder. Observe and record the properties, the final volume of the sample and the percent transmittance using the colorimeter.

- Wash your hands thoroughly before leaving the laboratory.

Calculations

Complete the following calculations.  Record your work and answers in your notebook.

- What percent of the original foul-water sample did you recover as pure water?

Percent of water purified = (vol. of water purified/ vol. of foul-water sample) (100)

- What percent of the filtrate recovered after each filtration?

Percent filtrate = (vol. of water oil water separation/ vol. of foul-water sample) (100)

Percent filtrate = (vol. of water sand filtration/ vol. of oil water separation) (100)

Percent filtrate = (vol. of water Charcoal filtration/ vol. of sand filtration) (100)

- Graph the Clarity (turbidity) readings in a bar graph and see which filter clarified the water the best.

- Graph the percentage of filtrate and see which filter uses up the most water.

- Looking at graph one which filter purified the foul water the best?

- Looking at graph two, which filter consumed most of the foul water?

- Looking at both graphs, which filter, is the best in cleaning up the foul water?